Description of 1-Wire protocol for slave devices with family code 0xCD
who enabled easy control more sensors and actor in one slave device

## Short description:
This data sheet contain description of 1-Wire protocol for slave devices with family code 0xCD (hex). This communication protocol, enable control multi sensors/actors devices (etc. temperature, humidity, pressure sensors with relays, switches, servos, step motor,...and much more).

Standard 1-wire communication is expanded communication protocol who enable control more sensor/actor in one device. This data sheet contain only this expand protocol. Basic 1-Wire communication is not mater of this document.
For this protocol exist driver for linux kernel and support for OFWS and arduino.
Next advantage is open-source library for easy create own 1-wire slave devices with many examples.
## Version:
Actual version is 1.0, a change in the protocol is not expected, but cannot be ruled out in the future.

Description division slave device into sections:
Every this slave device is division into section. Every section represents one sensor or actor. Every section has his own collection of registers determining type sensor or actor, his status and setting.
Read from or write into this registers is realized commands. The command may be for all device as find number of section, device description or for specific section as read/write actual value, user note,..

Scheme slave device and his sections:

Sekce
Sekce
 Number of section
Section 0
Triger min. alarm value 4B
Triger max. alarm value 4B
Producer section description 64B
User note 32B
 Producer device description 64B
 Actual value 4B
 Control registr 1B

Register description:
### Number of sections
Only for read, contain number of sections. Size1B.

Textual device description from producer 64B
Contain textual device description from producer. Size 64B.

control_byte register
determine properties of section. Size 1B. More at next table:

Bit 7	Bit 6	Bit 5	Bit 4	Bit 3	Bit 2	Bit 1	Bit 0
R/W	R/W	R	R		R	R	R/W
Max. alarm	Min. alarm	Alarm / flag	Data type memory, bool, u32, s32		alarm	zápis	čtení

Note. R – enable read, W – enable write, R/W – enable read and write

Bit description of control register:
Bit 0 - means whether actual_value register is for read=1 or not=0.
Writing 0 activate on save device reading sequence, it may take a while. Until the new value	is read correctly in the register with the current value, this bit is still 0, then it sets itself back	to 1. You can monitor the reading of this bit to see if the new value is already ready for	reading.
Bit 1 – means whether actual_value register is for write=1 or not=0. This bit is only for read. (its value is given by the manufacturer of the slave device)
Bit 2 – indicates whether the section has an alarm function 1=yes , 0=no. If not , bits 6and 7 lose their meaning. The alarm function can in some situations save unnecessary communication on the 1-Wire bus and speed up the response.

Bit 3-4 – these bits are only for read and indicate the resolution and type of section data using in actual_value, min. and max_alarm_value registers. See the next table:
Bit 4	Bit 3	Description	Numerc range	Data size
0	0	Without a value, the 32B space for the user description is used as memory for any data. Memory type.	always 0	4B
0	1	Only 0 or 1 (but transfer always all 4B)	0 to 1	4B
1	0	Unsigned 32 bit	0 to 4 294 967 295	4B
1	1	Signed 32bit	-2,147,483,648 to 2,147,483,647	4B

Bit 5 – alarm flag indicates that the section has fallen into alarm state. 1=section is in alarm, 0=section is not in alarm. This bit will be automatically reset after read from actual value register. Also if section data type (bit3=0 and bit4=0 in control register) is memory will be this bit automatically reset after read from user_note register (after read new data). If still remain alarm conditions then alarm will be again set.

Bit 6 – 1=on, 0=off alarm functionality for min. limit.

Bit 7 – 1=on, 0=off alarm functionality for max. limit.

In case:
- section has support alarms
- bought alarm (min. and max). is set in control register
- date types for this section is memory bits3=0 and bit4=0 of control resister (use user_note as memory page)
Then in that case so regardless of the min. or max. alarm values will be activated alarm after every data change. After successfully reading the contents of the memory, the alarm of the given section will be cancelled.

actual_value register
In this register is stored actual value of section. Data format depend on bit3 and bi4 of control register. Available are for options memory (register user_note is used as 32B memory page), bool, unsigned 32bit number and signed 32bit number. Whether writing is enabled depends on bit 1 of the control register. If bit 0 of the control register is equal to 0, then either the section does not support reading the current value, or an update of the current value has been requested and a valid value is not yet available.

min_alarm_value register
Here you can write or read the min. trigger value. Size is 4B, the format of the number used depends on bit3-4 of the control register, see the table above. The alarm condition will be evaluated based on this value only if the device supports it and this is enabled in bit 6 of the control register.

max_alarm_value register
Here you can write or read the min. trigger value. Size is 4B, the format of the number used depends on bit3-4 of the control register, see the table above. The alarm condition will be evaluated based on this value only if the device supports it and this is enabled in bit 6 of the control register.

description register

This register is read-only and contains a 64B section description written by the manufacturer.
The description describes the type, purpose and possibly the physical unit used by the sensor in the section. If the current value of this section is not directly in basic unit, but in some of its multiples, this multiple is also given there. A range of values can also be specified here .
For automatic classification of sections in automation systems, it is necessary to follow certain rules of this description when creating new devices:

1.) Keep format
type description [x_multiple unit] {value_for value_to}

Only the type is required, other parts of the description are optional.
- type – type sensor or actor, list of known types is below (this is the only mandatory item of the description the other items are only specifying).
- description – use only basic ascii coding space replace by “_”
- [x_multiple unit] fyzical unit. It is expected that slave devices use inexpensive simple MCUs, for which the processing of float numbers would be a difficult task, therefore all numbers are sent in integer form. If need may be use multiplier before name of unit (separed by one space). The unit multiple must be in this form eg x10, x100, x0.1, x.1,x1/5. The allowed units for each sensor type are listed below.
- {value_for value_to} the measuring range, or list allowed values {value1,value2,value3,..}

some examples :
Volt [x.1 V] {0 1000}
Temperature bottom_boiler [x.1 C] {-300 1500}	- measure temperature from range
-30,0 to 150,0C
Temperature top_boiler [x.1 C] {-300 1500}
Humidity air [%]
Volt set_output [x.01 V ] {200 1500}	- set output in volts from range 2,00 to 15,00V
Speed wind [Km/h ]
Switch relay1	- control relay1

2.) Use the sensor and unit type names listed here. If you would create your own device that you want to distribute publicly and you would not find a corresponding item in the list below, please contact us at info@seahu.cz . We will add the item after consultation to avoid duplicate items, the same applies to physical units.

Read or write values can be divided into three main categories:
SWITCH – only bool value 1=on or 0=off
VALUE – numerical value (range depends on control_byte register and range given in this description)
STRING – textual value (value is stored into
Note.: Read or write options is determined in control_byte register.

SWITCH
Switch description
Botton description
Read description
SmokeAlarm description
COalarm description
Pir description
D-OUT description
D-IN description
PIO description
Led description
Beep description
Lock description

VALUE
physical :
Temperature description [x.1 C] {-300 1500}
Humidity [%]
Pressure [x.1 Pa,Kpa,MPa ] {50 100}
Lighting [x.1 Lux]
UV	[mW/cm2,idx]
Weight [x.1 g,Kg]
Speed [x.1 m/s,Km/h]
Rotation [x.1 rpm]
Volume [%, db] {0 15}
Time [x.1 s,] {0 15}
electric:
Volt [x.1 mV, V ]
Current [x.1 mA, A]
Watt [x.1 mW, W]
Resistance [x.1 Ohm, KOhm]
Capacity [x.1 F,Ah]
Watt_meter[x.1 mWh,Wh,KWh,MWh]
chemical:
Ph [idx] {-7 7}
Concentration [x0.1 % ppm]
distance:
Distance [mm, cm, m ]
Cubic_capacity [ mm3, cm3, m3]
Bulk [x.1 ml, dcl, l]
Area [mm2, cm2, m2 ]
Angle [x0.1 deg,rad]
Width [deg]
Length [deg]
Height [x0.1 m]
common:
Value []
Meter [m]
Setter [%, °C, °F, m, W,..]
Percentage [%]
Counter [puls, pcs, W,...]
RGB [24b,48b,..]
RGBW [32b,54b,...]
ADC [16b,...]
DAC [12b,...]
PWM [12b,50%]
ID [10char, 12b, 15B]

STRING
String description {rows_x_columns}
the text is stored in the user_note register up to 31 characters (+ 1B = 0 as the end of the string). You must use multiple sections for more characters.

user_note register
This register enable up to 32 chars custom user description of section. For example, installation companies can by this register to mark their sensors in advance, which are then easily searchable in the control system (eg temperature sensor panel, temperature sensor boiler, switch pump ,.…)
Or if section have type=memory, than this register is used as memory (eg. for display text, RFID card code reader, code for IR receiver/transmitter, ….).

## Description of communication protocol:
Basic and bits level 1-Wire communication is described at https://en.wikipedia.org/wiki/1-Wire . Here described communication is only on messages level.

Each such device has its own unique 64 address (ROM address). The first 8 bits (1B) contain a 1-wire code of the 0xCD hex family. The next 48 bits (6 B) is a unique serial number. The last 8 bits (1 B) is the redundant cyclic sum of the first 56 bits.

64-Bit address (ROM address)
MSB				LSB
8-Bit CRC Code		48-Bit Serial Number		8-Bit Family Code (XX)
MSB	LSB	MSB	LSB	MSB	LSB

When manufacturing your own slave device, it is necessary to avoid possible duplication of addresses, so it is advisable to generate a serial number, for example, using a time stamp.

### Short rules description 1-Wire communication:
Devices is separed to one or more slave devices and one master device. The master device controls all communication. The slave devices wait and execute and respond to commands from the master device. All cummunication .Zařízení se dělí na master (hlavní) tj. ten co řídí komunikaci (většinou nějaká řídící jednotka, nebo 1-Wire brána) a slave (podřízený), který poslouchá mastera a když je vyzván tak mu odpovídá. All communication takes place on one data wire, to which voltage is applied via a resistor. The individual connected devices then short-circuit this wire when transmitting their signal and thus communicate.
From master view:
All start by reset signal from master (more longer short-circuit signal). This force all slave device to accept commands from master and simultaneously send shor signal back to master as proof of its existence (presence signal). From the reset responses, the master knows if anyone is present on the bus at all. If there are any slaves, we do not know how many there are. Therefore, the master sends a command with the code 0xF0 (Search rom), which starts a cleverly designed sequence of verifying the existence of individual bits from the 64-bit address, until it gradually searches for all present addresses.
Subsequently, the master chooses who he wants to communicate with. This is done by sending a reset signal again followed by a command with the code 0x55 (match rom) followed by the slave address with whom he wants to communicate The slave remembers that it was called for communication, after next reset don't must to again send the whole address. It can send only 0xA5 (resume) command to skip address. Or if slave device is only one on bus, than may skip addrres select by 0xCC (skip ROM) command. These basic command codes are called ROM COMMANDS and should be familiar to all slave devices.
They are followed by command codes and data that are specific and different for each device, also called FUNCTION COMMANDS.

The following is a list of supported commands:

### ROM COMMANDS
These are the standard 1-wire commands used in most 1-wire devices.
SEARCH ROM [F0h]	- search ROM address
READ ROM [33h]	- read ROM address
(useful only with one slave device on bus)
MATCH ROM [55h]	- the master chooses with whom he will communicate
SKIP ROM [CCh]	- the master skips the address selection
(useful only with one slave device on bus)
RESUME [A5h]	- master device resume communication with last selected slave	device, without sending address
ALARM SEARCH [Ech]	- similar to SEARCH ROM, but only devices in an alarm state	respond to the search

### FUNCTION COMMANDS
Commands specific to each family (given by the family code) of the slave device. The function command always follows after ROM commands. These commands are used to read and write to the slave device registers.
For this device family, the function commands can be divided for commands to whole device or commands to apply to specific section. For reasons of avards to possible errors on the bus, a 16-bit CRC sum is always sent at the end of the communication, which is starts counting from the byte with the function command.
After completing the function command, the slave device is ready to receive the next function command. In this way, for example, the current values ​​of all sections can be read sequentially without the master having to send more reset signals.
For clarity are listed below the codes of these commands including their sequence of 1-Wire communication .
### FUNCTION COMMANDS structure of query and answer:
Legend of communication direction:

Master --> slave	Slave --> master	Programing/sampling

Legenda used symbols:

SYMBOL	DESCRIPTION
RST	1-Wire reset pulse, generated by master
PD	1-Wire presence pulse, generated by slave
Select	Command for select slave (MATCH ROM, RESUME or SKIP ROM according to the situation ).

READ PRODUCT DESCRIPTION 64B [F1h]
RST	PD	Select	[F1h]	64B (data) Textual product description	2B / CRC16 form 0xF1 and data

If the CRC do not match, the reading must be repeated.

READ NUMBER OF SECTIONS [F2h]
RST	PD	Select	[F2h]	1-B (data) nuber of sections	2B / CRC16 from 0xF1 and data

If the CRC do not match, the reading must be repeated.

READ FROM CONTROL REGISTER [F3h]
RST	PD	Select	[F3h]	1-B section number	1B (data) the contents of the control register	2B CRC16 from 0xF3, section number and data

If the CRC do not match, the reading must be repeated.
The meaning of the individual bits of the control register is described above.

WRITE INTO CONTROL REGISTER [53h]
RST	PD	Select	[53h]	1B section number	1-B (data ) new content of control register	2B / CRC16 from [53h] , section number and new content of control register	1B / confirmation [AAh/FFh]

If confirmation byte != AAh, then the write must be repeated.
The meaning of the individual bits of the control register is described above.

COMMAND FOR START NEW MEASURE OR FORCE ACCEPT NEW VALUES [44h]
RST	PD	Select	[44h]	Section number, [FFh] mean all sections	2-Byte 16bit CRC from [44h] ans section number	1B / confirmation [AAh/FFh]

If confirmation byte != AAh, then the write must be repeated. Section number [FFh] force actualize actual values into all sections.
Note: Most output devices apply new values immediately, but sometimes is necessary to apply new values from multiple sections at once (e.g. if necessary to update a color who has separate RGB parts in separate sections without flickering).

READ FROM SECTION ACTUAL VALUE REGISTER [F5h]
RST	PD	Select	[F5h]	1B section number	4B data	2B / CRC16 from [F5h] section number and data

If the CRC do not match, the reading must be repeated. The format of the binary data depends on the section control register.

WRITE TO SECTION ACTUAL VALUE REGISTER [55h]
RST	PD	Select	[55h]	1B section number	4B / data	2B / CRC16 from [55h] section number and data	1B / confirmation [AAh/FFh]

If confirmation byte != AAh, then the write must be repeated. The format of the binary data depends on the section control register. The control register also contain information whether section have possibility to write into actual value register. If not, the communication will take place, but any effect on the slave device.

READ FROM TRIGGER MIN. ALARM VALUE REGISTER [FAh]
RST	PD	Select	[FAh]	1B section number	4B data	2B / CRC16 from [FAh] section number and data

If the CRC do not match, the reading must be repeated. The format of the binary data depends on the section control register.

READ FROM TRIGGER MAX. ALARM VALUE REGISTER [FBh]
RST	PD	Select	[FBh]	1B section number	4B data	2B / CRC16 from [FBh] section nuber and and data

If the CRC do not match, the reading must be repeated. The format of the binary data depends on the section control register.

WRITE INTO TRIGGER MIN. ALARM VALUE REGISTER [5Ah]
RST	PD	Select	[5Ah]	1B sectrion number	4B data	2B / CRC16 from [5Ah] section number and data	If CRC is OK then write into EEPROM ~100µms	1B / confirmation [AAh/FFh]

If confirmation byte != AAh, then the write must be repeated. The format of the binary data depends on the section control register. New value is write into EEPROM.

WRITE INTO TRIGGER MAX. ALARM VALUE REGISTER [5Bh]
RST	PD	Select	[5Bh]	1B section number	4 B data	2B / CRC16 from [5Bh] section number and data	If CRC is OK, then write into EEPROM 100µms	1B / Confirmation [AAh/FFh]

If confirmation byte != AAh, then the write must be repeated. The format of the binary data depends on the section control register. New value is write into EEPROM.

READ FROM PRODUCER SECTION DESCRIPTION REGISTER [F7h]
RST	PD	Select	[F7h]	1B section number	Read from PROGMEM / 100µms	64 B data	2B / CRC16 from [F7h] section number and data

If the CRC do not match, the reading must be repeated. The format of the binary data depends on the section control register.
Manufacturers of slave devices should follow the prescribed format of description of sensors or elements, see. above description of the manufacturer's text description register.

READ FROM USER NOTE REGISTER [F8h]
RST	PD	Select	[F8h]	1B section number	Read from PROGMEM / 50µms	32 B / data	2B / CRC16 from [F8h] section number and data

If the CRC do not match, the reading must be repeated.

WRITE INTO USER NOTE REGISTER [58h]
RST	PD	Select	[58h]	1B section number	32 B / data	2B / CRC16 from [58h] section nzmber and data	If CRC is OK then write into EEPROM 100µms	1B / Confirmation [AAh/FFh]

If confirmation byte != AAh, then the write must be repeated.
The user description is written to the EEPROM, so it is available even after the slave device is disconnected from the power supply. It is recommended to use only basic ascii encoding in the description.
In some cases, instead of writing to the EEPROM, the data can be used for display on the slave device display, or just stored in RAM. In this case, the data memory type should be set in the control register and the text description of the section from the manufacturer should have the following form:
string description {radek_x_sloupec}
memory description {32B}

### FUNCTION COMMANDS with detailed examples of 1-Wire communication:
READ PRODUCT DESCRIPTION 64B [F1h]
MASTER MODE / TX- write RX- read	DATA (LST FRIST)	COMMENTS
TX	(reset)	Reset pulse
RX	(presence)	Presence pulse (confirmation of presence)
TX	55h	Command for choice slave device by ROM address.
TX	<8 byte ROM ID>	ROM address
TX	F1hCommand -	Command - read producer description.
RX	<64B Data>	read data 64 bytes. / Data contain textual description of slave device (e.g. producer, type designation, version, short description).
RX	<2 byte CRC16>	2-Byte CRC16 from command and datat.
TX	(reset)	Reset pulse. (new cycle)

If the CRC do not match, the reading must be repeated.

READ NUMBER OF SECTIONS [F2h]
MASTER MODE / TX- write RX- read	DATA (LST FRIST)	COMMENTS
TX	(reset)	Reset pulse
RX	(presence)	Presence pulse (confirmation of presence)
TX	55h	Command for choice slave device by ROM address.
TX	<8 byte ROM ID>	ROM address
TX	F2h	Command - read number of section
RX	<1 byte Data>	Number of sections.
RX	<2 byte CRC16>	CRC16 from F2h command and data
TX	(reset)	Reset pulse. (new cycle)

If the CRC do not match, the reading must be repeated.

READ FROM CONTROL REGISTER [F3h]
MASTER MODE / TX- write RX- read	DATA (LST FRIST)	COMMENTS
TX	(reset)	Reset pulse
RX	(presence)	Presence pulse (confirmation of presence)
TX	55h	Command for choice slave device by ROM address.
TX	<8 byte ROM ID>	ROM address
TX	F3h	Command - read from control register
TX	<1 byte Číslo sekce>	Section number
RX	<1 byte Data>	1B content of control register
RX	<2 byte CRC16>	2-Byte CRC16 from F3h command, section number and data
TX	(reset)	Reset pulse. (new cycle)

If the CRC do not match, the reading must be repeated.

WRITE INTO CONTROL REGISTER [53h]
MASTER MODE / TX- write RX- read	DATA (LST FRIST)	COMMENTS
TX	(reset)	Reset pulse
RX	(presence)	Presence pulse (confirmation of presence)
TX	55h	Command for choice slave device by ROM address.
TX	<8 byte ROM ID>	ROM address
TX	53h	Command – write into control register
TX	<1 byte Číslo sekce>	Section number
TX	<1 byte Data>	Data byte - new content of control register
TX	<2 byte CRC16>	2-Byte CRC16 from command 53h, section number and data
RX	AAh	Read confirmation byte (AAh = success)
TX	(reset)	Reset pulse. (new cycle)

If confirmation byte != AAh, then the write must be repeated.
The meaning of the individual bits of the control register is described above.

COMMAND FOR START NEW MEASURE OR FORCE ACCEPT NEW VALUES [44h]
MASTER MODE / TX- write RX- read	DATA (LST FRIST)	COMMENTS
TX	(reset)	Reset pulse
RX	(presence)	Presence pulse (confirmation of presence)
TX	55h	Command for choice slave device by ROM address.
TX	<8 byte ROM ID>	ROM address
TX	44h	Command – for start new measure or force accept new value
TX	<1 byte Číslo sekce>	Section number, [FFh] mean for all sections
TX	<2 byte CRC16>	2-Byte CRC16 from command 44h and section number
RX	AAh	Read confirmation byte (AAh = success)
TX	(reset)	Reset pulse. (new cycle)

If confirmation byte != AAh, then the write must be repeated.

READ FROM SECTION ACTUAL VALUE REGISTER [F5h]
MASTER MODE / TX- write RX- read	DATA (LST FRIST)	COMMENTS
TX	(reset)	Reset pulse
RX	(presence)	Presence pulse (confirmation of presence)
TX	55h	Command for choice slave device by ROM address.
TX	<8 byte ROM ID>	ROM address
TX	F5h	Command – read section actual value
TX	<1 byte Číslo sekce>	Section number
RX	<4 byte Data>	Read data, format depend on value from control register
RX	<2 byte CRC16>	2-Byte CRC16 from command F5h section number and data
TX	(reset)	Reset pulse. (new cycle)

If the CRC do not match, the reading must be repeated. The format of the binary data depends on the section control register.
WRITE TO SECTION ACTUAL VALUE REGISTER [55h]
MASTER MODE / TX- zápis RX- čtení	DATA (LST FRIST)	COMMENTS
TX	(reset)	Reset pulse
RX	(presence)	Presence pulse (confirmation of presence)
TX	55h	Command for choice slave device by ROM address.
TX	<8 byte ROM ID>	ROM address
TX	55h	Command – write to section actual value
TX	<1 byte Číslo sekce>	Section number
TX	<4 byte Data >	Write data, format depend on value from control register
TX	<2 byte CRC16>	2-Byte CRC16 from command 55h, section number and data
RX	AAh	Read confirmation byte (AAh = success)
TX	(reset)	Reset pulse. (new cycle)

If confirmation byte != AAh, then the write must be repeated.

READ FROM TRIGGER MIN. ALARM VALUE REGISTER [FAh]
MASTER MODE / TX- write RX- read	DATA (LST FRIST)	COMMENTS
TX	(reset)	Reset pulse
RX	(presence)	Presence pulse (confirmation of presence)
TX	55h	Command for choice slave device by ROM address.
TX	<8 byte ROM ID>	ROM address
TX	FAh	Command – read from trigger min. alarm value register
TX	<1 byte Číslo sekce>	Section number
RX	<4 byte Data>	Read data, format depend on value from control register
RX	<2 byte CRC16>	2-Byte CRC16 from command Fah, section number and data
TX	(reset)	Reset pulse. (new cycle)

If the CRC do not match, the reading must be repeated.

READ FROM TRIGGER MAX. ALARM VALUE REGISTER [FBh]
Same as previous only instead of FAh command code is used FBh code.

WRITE INTO TRIGGER MIN. ALARM VALUE REGISTER [5Ah]
MASTER MODE / TX- write RX- read	DATA (LST FRIST)	COMMENTS
TX	(reset)	Reset pulse
RX	(presence)	Presence pulse (confirmation of presence)
TX	55h	Command for choice slave device by ROM address.
TX	<8 byte ROM ID>	ROM address
TX	5Ah	Command – write into trigger min. alarm value register
TX	<1 byte Číslo sekce>	Section number
TX	<4 byte Data >	Write data, format depend on value from control register
TX	<2 byte CRC16>	2-Byte CRC16 from command 5Ah, section number and data
100µms wait fro write data into EEPROM
RX	AAh	Read confirmation byte (AAh = success)
TX	(reset)	Reset pulse. (new cycle)

If confirmation byte != AAh, then the write must be repeated.

WRITE INTO TRIGGER MIN. ALARM VALUE REGISTER [5Bh]
Same as previous only instead of 5Ah command code is used 5Bh code.

READ FROM PRODUCER SECTION DESCRIPTION REGISTER [F7h]
MASTER MODE / TX- write RX- read	DATA (LST FRIST)	COMMENTS
TX	(reset)	Reset pulse
RX	(presence)	Presence pulse (confirmation of presence)
TX	55h	Command for choice slave device by ROM address.
TX	<8 byte ROM ID>	ROM address
TX	F7h	Command – read from producer section description register
TX	<1 byte Číslo sekce>	Section umber
RX	<64B Data>	Read 64B of textual producer description of section. The recommended format is described above
RX	<2 byte CRC16>	2-Byte CRC16 from command F7h, section number and data
TX	(reset)	Reset pulse. (new cycle)

If the CRC do not match, the reading must be repeated.

READ FROM USER NOTE REGISTER [F8h]
MASTER MODE / TX- write RX- read	DATA (LST FRIST)	COMMENTS
TX	(reset)	Reset pulse
RX	(presence)	Presence pulse (confirmation of presence)
TX	55h	Command for choice slave device by ROM address.
TX	<8 byte ROM ID>	ROM address
TX	F8h	Command – read from user note register
TX	<1 byte Číslo sekce>	Section umber
50µms wait for read from EEPROM
RX	<32B Data>	Read 32B of user note
RX	<2 byte CRC16>	2-Byte CRC16 from command F8h, section nzmber anda data
TX	(reset)	Reset pulse. (new cycle)

If the CRC do not match, the reading must be repeated.

WRITE INTO USER NOTE REGISTER [58h]
MASTER MODE / TX- write RX- read	DATA (LST FRIST)	COMMENTS
TX	(reset)	Reset pulse
RX	(presence)	Presence pulse (confirmation of presence)
TX	55h	Command for choice slave device by ROM address.
TX	<8 byte ROM ID>	ROM address
TX	58h	Command – write into user note register
TX	<1 byte Číslo sekce>	Section umber
TX	<32B Data >	Write 32B of user note stored into EEPROM or alternative as general RAM memory. Depends on control register.
TX	<2 byte CRC16>	2-Byte CRC16 from command 58h, section number and data
100µms wait to write data into EEPROM
RX	AAh	Read confirmation byte (AAh = success)
TX	(reset)	Reset pulse. (new cycle)

If confirmation byte != AAh, then the write must be repeated.
The user description is written to the EEPROM, so it is available even after the slave device is disconnected from the power supply. It is recommended to use only basic ascii encoding in the description.
In some cases, instead of writing to the EEPROM, the data can be used for display on the slave device display, or just stored in RAM. In this case, the data memory type should be set in the control register and the text description of the section from the manufacturer should have the following form:
string description {radek_x_sloupec}
memory description {32B}
### More information:
http://www.seahu.cz
https://en.wikipedia.org/wiki/1-Wire
http://owfs.org
https://github.com/seahu/SH019 – source code examples for ARDUINO, LINUX a OWFS

### Writer:
Ing. Ondřej Lyčka leden 2021
Document version: 1.00