SH026c
1-WIRE interface for distance ultrasonic sensors
HC-SR04, HC-SR05, HY-SR05 or JSN-SR04T

1-WIRE INTERFACE FOR ULTRASONIC DISTANCE SENSOR
DESCRIPTION
This is 1-wire interface for HC-SR04, HC-SR045, HY-SR05 or JSN-SR04T ultrasonic distance sensor (meter). Enable measure depend on sensor from 2cm to 5,2m.
The use universal board Seahu SH026 with firmware specialized for DTH22 sensor.

FEATURES
- 1-Wire ESD protection
- led indication
- enable set measure correction value
- enable set alarm condition for measured distance
- enable save actual and setting values to EEPROM
- software support for arduino, linux kernel and OWFS project

HC-SR04 sensor:
- distance:	from 2cm to 450cm
- accuracy:	+/- 3 mm
HC-SR05 sensor:
- distance:	from 2cm to 520cm
- accuracy:	+/- 2mm
HY-SR05 sensor:
- distance:	from 2cm to 520cm
- accuracy:	+/- 2mm
JSN-SR04T waterproof sensor:
- distance:	from 25cm to 450cm
- accuracy:	+/- 5mm

Note: SH026c interface round measured distance to whole cm.

CONNECTION
2
3

`

GND
PIO
+5V
A-IN
+5V
GND
+5V
PIO
A-IN
PIO
GND
+5V
A-IN
PIO
A-IN

`
`
`

4

1

Connection:
Sensor	SH026c
Vcc	+5V
Trig	PIO
Echo	A-IN
Gnd	GND

1 – conector RJ12 for 1-wire bus
2 – jumper
On – join 1 and 5 pins of RJ12 connector
enable 5V power driver from pin 5
3 – indication led
4 – cavity mouldings

PIN CONFIGURATION RJ12 CONECTOR
PIN / 1 / 2 / 3 / 4 / 5 / 6 / Looking into Female RJ12 / Connector	SIGNAL / NAME	DESCRIPTION
1	VDD	5 V DC
2	GND	Ground
3	OW	1-Wire Data (only 5V level logic)
4	GND	Ground
5	N.C. / [VDD]	If jumper ON / then 5V DC !!! no more !!! / else No Connection
6	N.C.	No Connection

POWER SUPPLY:
Form 1-wire bus by default pin 1 of RJ12 connector. Some one-wire devices use 4-wire cable with power pin 5 instead pin 1 on RJ12 connector. In this case may use jumper who join this pines.

1-WIRE:
Use only 5V logic level.

Family Code: 0xCD
based on arduino 1-Wire slave devices as mulstisensors/actors project more at https://github.com/seahu/seahu_CD/tree/master/Documentation
The device use 8 sections. The sections description is bellow.

Device description :SEAHU SH026c 1-Wire to ultrasonic distance sensor
Number of section: 4
Sections:
Section 0: Distance [cm]
measured distance in cm
value type: number integer 32bit
Section 1: Distance [cm] distance corection
correction of distance in cm
value type: number integer 32bit
Section 5: led identification
identify of 1-Wire device
value type: bool value (only 0 or 1) as unsigned number integer 32bit
1=on
0=off
Section 6: save
save actual values (for read always =0)
value type: bool value (only 0 or 1) as unsigned number integer 32bit
1= start save
0= do nothing

SOFTWARE SUPPORT:
The device is supported in next software platforms.
Arduino as custom library:
https://github.com/seahu/seahu_CD/tree/master/arduino/OneWireMaster0xCD

Linux kernel as kernel module
https://github.com/seahu/seahu_CD/tree/master/linux-kernel-module

OWFS (one wire file system) as own clone:
https://github.com/seahu/owfs

More information
web page seahu	http://www.seahu.cz

Writer:
Ing. Ondřej Lyčka in January 2022

version document: 1.01